## Slide 1
Type-C, USB PD 3.0 PPS, QC4+
Total Solution
Eilian Liu
Product Marketing
June 29, 2018
Leadtrend Confidential for Big-Bit Only

## Slide 2: LD6610 Certification
Qualcomm: Quick Charge C4.0
USB IF: PD2.0/PD3.0/PPS

## Slide 3: USB Type-C™ and USB PD Testing
USB PD Compliance Test Equipment
QuadraMAX (Power Brick PPS )
http://www.usb.org/developers/estoreinfo/
Communication Engine MOI
MQP PDT
  http://www.mqp.com/pd.htm
Granite River Labs - GRL-USB-PD Oscilloscope based and USB-PD-C1 USB Type-C Test Controller Compliance Solution
  http://graniteriverlabs.com/usb-pd
Granite River Labs - GRL-USB-PD-C2 USB Type-C Power Delivery Tester
  http://graniteriverlabs.com/usb-pd-c2/
Teledyne LeCroy - Voyager M310P Protocol Analyzer / Exerciser / Compliance Test Platform
  http://teledynelecroy.com/protocolanalyzer/protocoloverview.aspx?seriesid=556&capid=103&mid=511
Deterministic MOI
Ellisys USB Explorer™ 350 Protocol Analyzer, Generator, and Compliance Test System
  http://ellisys.com/products/usbex350/index.php

## Slide 4: USB Power Delivery PPS Certification Flow
1. PPS Specification Document:
- USB_PD_R3_0 V1.1 20180207
- USB PD R3 0 V1 1 ECN PPS Current Requirements above Nominal Prog Voltage 20170918
- USB PD R3.0 V1.1 ECN APDO Min Voltage
- USB PD R3.0 V1.1 ECN PPS Status measurements
- USB PD R3.0 V1.1 iPpsCLTransient clarification 20180207
http://www.usb.org/developers/docs/
2. PPS Test Document: USB-C_Source_Power_Test_Specification_2018_01_03 (Revision 0.74)
http://www.usb.org/developers/compliance/usbcpd_testing/
3. PPS Test Equipment: QuadraMAX
http://www.usb.org/developers/estoreinfo

## Slide 5: PPS Programmable Voltage and Current Limit

## Slide 6: PPS Voltage and Current Accuacy

## Slide 7
2.8A
1.4A
Output Voltage Transition
PPS Mode ( SPT. 6 PPS Voltage Step Test ):
Workshop 107 TID025
VST: PASS
A. Purpose:
The PPS Step Test verifies that when a source port makes a contract using an APDO its output follows the monotonicity and tolerance requirements from USB PD spec section 7.1.4.3.
This test is required for all USB PD ports that advertise APDO capabilities.
This is a single port test at this time.
This is a USB PD 3.0 test only
C. Step Size Conditions:
20mV
100mV
500mV
D. Operating Current Conditions:
1 A
APDO Maximum Current / 2 + 500 mA
APDO Maximum Current

## Slide 8: PPS Constant Power Mode

## Slide 9: LD6610 Solution Example: Type-C Power Adapter / Mobile Charger
- Provides Type-C solution with Power Delivery 3.0 (PD 3.0) with programmable power supply support and Quick Charge 4.0 (QC 4.0)
- Min. V&I resolution 10mV/25mA for PPS
- Programmable OCP, OVP, UVP, OTP
LD576X Value
LD852X Value
LD661X Value
- LD8523 (MP): Vout 3V~11V
DET pin rating 85V
- LD8525 (MP): Vout 5V~20V
DET pin rating 150V
- LD8526(ES): Vout 3V to 21V,
DET pin rating 200V
- Ultra low Green Mode current
< 250uA
- X-Cap Discharge, No Load <30mW
- OCP/OPP/OSCP/CS_OTP Protections
- VCC Ratting
LD5763 70V
LD5765 80V
- Adaptive Loop Gain for Loop Stability
- Adaptive Current Limit to meet LPS

## Slide 10
Leadtrend
LD5763
SSR PWM Controller
Features:
PKG Tape:
UHV 750V.
X-Cap Discharge, No Load <30mW
OCP/OPP/OSCP/CS_OTP Protections
VCC Ratting around
  LD5763 = 70V
Adaptive Loop Gain for Loop Stability
Adaptive Current Limit to meet LPS
+300mA/-800mA Driving Capability
Built- in Two Level Frequency on HV pin (Option)
SOP-8 and SOP-7

## Slide 11: LD6610 PD3.0 PPS Reference Circuit
Size 48mm(L) x 36 (W)mm x 18mm(H)
DBPDP1704B

## Slide 12: LD6610 Solution Example: Car Charger，Multi- Port Wall Adapter
Car Charger
Wall Adapter 1A+1C
NB compatible testing for PD accessories
Apple Mac Air, Macbook Pro, iPhone X/8/Plus
Huawei
Lenovo
HP
Dell
NINTENDO SWITCH

## Slide 13: Accelerate Time-to-Market With Reference Designs
1. 12 V is required for Quick Charge 2 and Quick Charge 3 2. Quick Charge 4 compatible the latest USB PD programmable power supply rules 3. Programmable power supply (PPS), four APDOs a) 3.3V-5.9V, b) 3.3V-11V, c) 3.3V-16V, d) 3.3V-20V. Optional indicates a Host OEM decision 4. under development 5. Recommend LD5765 for 3.3V-16V or 3.3V-20V voltage level 6. LD3103 integrated PMOS load switching
Application | PWM | SR | PD Controller | QC2.0 QC3.0 | QC4.02 | 5V Only | PD3.0 | PPS | Output Voltage Level
15W 5V Only Travel Charger | LD5512 (PSR) | LD8923 (MOSFET) | LD8200S or LD31036 |  |  | ü |  |  | 5V
 | LD5523 (PSR) | LD8923 (MOSFET) | LD8200S or LD31036 |  |  | ü |  |  | 5V
27W QC4.0 Travel Charger | LD57635 | LD8523 | LD6610GQMW | ü | ü |  | ü | ü | 5V, 9V, 3.3V- 5.9V3, 3.3V- 11V3, 12V1
Notebook Adapter 45W | LD5763 | LD8525 | LD6610GF |  |  |  | ü |  | 5V, 9V, 15V, 20V
Notebook Adapter 61W | LD5763 | LD8525 | LD6610GF |  |  |  | ü |  | 5V, 9V, 15V, 20V
Dual Port Wall Adapter 45W4 | LD57655 | LD8526 (ES) | LD6610GQMW | ü | ü |  | ü | ü | 5V, 9V, 12V, 15V, 20V 3.3V- 5.9V3, 3.3V- 11V3 3.3V- 16V3

## Slide 14
27W QC4.0 Travel Charger
Bottom View
Top View
36 mm
Side View
48 mm
Rear View
21 mm
LD5763
LD6610
LD8523
12.2 W / inch3

## Slide 15
27W QC4.0 Travel Charger Efficiency
Input Voltage | 115 VAC / 60 Hz | 230 VAC / 50 Hz
Output Current | 100 %, 75 %, 50 %, 25 %, 10 % of Full Load | 
Measured Point of Output Voltage | End of PCB | 
Duration of Burn-in | 30 Minutes | 
Requirement | CoC Tier 2 | 
27W QC4.0 Travel Charger

## Slide 16
27W QC4.0 Travel Charger Efficiency ( Cont. )
VIN,AC ( V / Hz ) | Mode | VBUS,SET ( V ) | VBUS,PCB ( V ) | IOUT ( A ) | PBUS,PCB ( W ) | PIN ( W ) | η ( % ) | ηAV,4-Points ( % ) | Requirement ( % )
115 / 60 | PD 3.0 | 5 | 5.0809 | 2.9940 | 15.212 | 17.373 | 87.562 | 88.705 | > 81.84
 |  |  | 5.0860 | 2.2440 | 11.413 | 12.770 | 89.373 |  | 
 |  |  | 5.0907 | 1.4960 | 7.616 | 8.517 | 89.417 |  | 
 |  |  | 5.0951 | 0.7480 | 3.811 | 4.308 | 88.466 |  | 
 |  |  | 5.0977 | 0.2960 | 1.509 | 1.787 | 84.439 | ─ | > 72.48
 |  | 9 | 9.1011 | 2.9940 | 27.249 | 30.535 | 89.238 | 89.684 | > 87.30
 |  |  | 9.1061 | 2.2440 | 20.434 | 22.607 | 90.388 |  | 
 |  |  | 9.1097 | 1.4960 | 13.628 | 15.140 | 90.014 |  | 
 |  |  | 9.1135 | 0.7480 | 6.817 | 7.651 | 89.098 |  | 
 |  |  | 9.1160 | 0.2960 | 2.698 | 3.190 | 84.587 | ─ | > 77.30
 | PPS | 3.3 | 3.3067 | 2.9510 | 9.758 | 11.356 | 85.929 | 87.398 | > 78.93
 |  |  | 3.3170 | 2.2460 | 7.450 | 8.444 | 88.228 |  | 
 |  |  | 3.3276 | 1.4980 | 4.985 | 5.645 | 88.304 |  | 
 |  |  | 3.3385 | 0.7480 | 2.497 | 2.866 | 87.132 |  | 
 |  |  | 3.3448 | 0.2960 | 0.990 | 1.176 | 84.189 | ─ | > 69.66
 |  | 11 | 11.1015 | 2.4110 | 26.766 | 29.706 | 90.102 | 89.405 | > 87.30
 |  |  | 11.1039 | 1.8410 | 20.442 | 22.712 | 90.007 |  | 
 |  |  | 11.1072 | 1.2260 | 13.617 | 15.237 | 89.371 |  | 
 |  |  | 11.1103 | 0.6130 | 6.811 | 7.727 | 88.140 |  | 
 |  |  | 11.1120 | 0.2510 | 2.789 | 3.388 | 82.323 | ─ | > 77.30
 | QC 3.0 | 3.6 | 3.5999 | 3.0000 | 10.800 | 12.470 | 86.605 | 87.971 | > 79.56
 |  |  | 3.6078 | 2.2500 | 8.118 | 9.140 | 88.813 |  | 
 |  |  | 3.6151 | 1.5000 | 5.423 | 6.107 | 88.794 |  | 
 |  |  | 3.6225 | 0.7500 | 2.717 | 3.099 | 87.669 |  | 
 |  |  | 3.6271 | 0.3000 | 1.088 | 1.270 | 85.680 | ─ | > 70.27
 |  | 12 | 12.0240 | 2.2460 | 27.006 | 29.958 | 90.146 | 89.439 | > 87.30
 |  |  | 12.0270 | 1.6870 | 20.290 | 22.542 | 90.008 |  | 
 |  |  | 12.0300 | 1.1250 | 13.534 | 15.117 | 89.527 |  | 
 |  |  | 12.0330 | 0.5620 | 6.763 | 7.678 | 88.077 |  | 
 |  |  | 12.0340 | 0.2250 | 2.708 | 3.279 | 82.575 | ─ | > 77.30

## Slide 17
27W QC4.0 Travel Charger Efficiency ( Cont. )
VIN,AC ( V / Hz ) | Mode | VBUS,SET ( V ) | VBUS,PCB ( V ) | IOUT ( A ) | PBUS,PCB ( W ) | PIN ( W ) | η ( % ) | ηAV,4-Points ( % ) | Requirement ( % )
230 / 50 | PD 3.0 | 5 | 5.0812 | 2.9940 | 15.213 | 17.147 | 88.722 | 87.670 | > 81.84
 |  |  | 5.0867 | 2.2440 | 11.415 | 12.908 | 88.430 |  | 
 |  |  | 5.0912 | 1.4960 | 7.616 | 8.671 | 87.838 |  | 
 |  |  | 5.0957 | 0.7480 | 3.812 | 4.448 | 85.692 |  | 
 |  |  | 5.0985 | 0.2960 | 1.509 | 1.888 | 79.934 | ─ | > 72.48
 |  | 9 | 9.1013 | 2.9940 | 27.249 | 30.097 | 90.538 | 89.662 | > 87.30
 |  |  | 9.1060 | 2.2440 | 20.434 | 22.664 | 90.160 |  | 
 |  |  | 9.1097 | 1.4960 | 13.628 | 15.196 | 89.682 |  | 
 |  |  | 9.1135 | 0.7480 | 6.817 | 7.723 | 88.267 |  | 
 |  |  | 9.1158 | 0.2960 | 2.698 | 3.324 | 81.176 | ─ | > 77.30
 | PPS | 3.3 | 3.3063 | 2.9510 | 9.757 | 11.281 | 86.490 | 85.460 | > 78.93
 |  |  | 3.3170 | 2.2460 | 7.450 | 8.626 | 86.367 |  | 
 |  |  | 3.3275 | 1.4980 | 4.985 | 5.800 | 85.941 |  | 
 |  |  | 3.3384 | 0.7480 | 2.497 | 3.007 | 83.044 |  | 
 |  |  | 3.3448 | 0.2960 | 0.990 | 1.258 | 78.701 | ─ | > 69.66
 |  | 11 | 11.1009 | 2.4110 | 26.764 | 29.561 | 90.539 | 89.435 | > 87.30
 |  |  | 11.1046 | 1.8410 | 20.444 | 22.676 | 90.155 |  | 
 |  |  | 11.1076 | 1.2260 | 13.618 | 15.229 | 89.421 |  | 
 |  |  | 11.1111 | 0.6130 | 6.811 | 7.773 | 87.625 |  | 
 |  |  | 11.1125 | 0.2510 | 2.789 | 3.495 | 79.807 | ─ | > 77.30
 | QC 3.0 | 3.6 | 3.5999 | 3.0000 | 10.800 | 12.416 | 86.982 | 86.015 | > 79.56
 |  |  | 3.6078 | 2.2500 | 8.118 | 9.317 | 87.126 |  | 
 |  |  | 3.6153 | 1.5000 | 5.423 | 6.265 | 86.559 |  | 
 |  |  | 3.6225 | 0.7500 | 2.717 | 3.258 | 83.391 |  | 
 |  |  | 3.6270 | 0.3000 | 1.088 | 1.358 | 80.125 | ─ | > 70.27
 |  | 12 | 12.0240 | 2.2460 | 27.006 | 29.782 | 90.679 | 89.543 | > 87.30
 |  |  | 12.0270 | 1.6870 | 20.290 | 22.479 | 90.260 |  | 
 |  |  | 12.0300 | 1.1250 | 13.534 | 15.106 | 89.592 |  | 
 |  |  | 12.0330 | 0.5620 | 6.763 | 7.716 | 87.643 |  | 
 |  |  | 12.0350 | 0.2250 | 2.708 | 3.392 | 79.831 | ─ | > 77.30

## Slide 18
27W QC4 No Load Power Consumption
Input Voltage | 115 VAC / 60 Hz | 230 VAC / 50 Hz
Output Current | 0 A ( Disconnect USB Type-C Cable ) | 
Requirement | CoC Tier 2 | 
VIN,AC ( V / Hz ) | PIN ( mW ) | Requirement ( mW )
115 / 60 | 19 | < 75
230 / 50 | 22 | 
No Load Standby Power Consumption is < 30 mW @ 230 VAC

## Slide 19: PD3.0 PPS / QC4 Certification and Testing Tools
Leadtrend communication Engine MOI: GRL C2, Ellisys, QuadraMax
DBPDP1704B - PD 3.0 / QC 4.0+ Test Kit
Wall adapter or Accessories
Type C Cable
DBPD1704B
Power Meter
&
Eload